    FTP access permission

Step :1 Block ftp permission for all IP

   We can block the ftp port diffrenet way in squid proxy server. By blocking the ftp port no one could not access the ftp particular lan network.

To open the squid conf file and block the ftp port 21 via ACLs. Let see step by step configuration
in squid proxy server.

ACL based blocking the FTP port

Open the squid.conf file

#vim /etc/squid/squid.conf

add the following line

#create acl for ftp port
acl Bad_ports port 21

#block the port
http_access deny Bad_ports

save and close the squid.conf file.

#Restart the squid service

service squid restart

Now we can’t access the ftp port from any ip address within the network.

ACL ftp & IP address based Allow

Create the acl file for ftp port squid

vim /etc/squid/allowftp.acl

To put the ftp port 21 then save and close the file.

Open the squid.conf file

#vim /etc/squid/squid.conf
add the following line

#create acl for IP address
acl allowip src 192.168.2.21

#create acl for ftp port
acl allowftp port “/etc/squid/allowftp.cal”

#Allow the access
http_access allow allowip allowftp

save and close the squid.conf file.

#Restart the squid service

service squid restart

Now we can access ftp port only particular ip address of the network.

Step :2 Allow the ftp access for particular Ip with particular website

Create the acl file for ftp Domain/website

vim /etc/squid/allowfto.domain.acl

To put the ftp domain/website then save and close the file.

Open the squid.conf file

#vim /etc/squid/squid.conf
add the following line

#create acl for IP address
acl allowip src 192.168.2.21

#create acl for ftp port
acl allowftp port “/etc/squid/allowftp.cal”

#Allow the access
http_access allow allowip allowftp allowftpdomain

save and close the squid.conf file.

#Restart the squid service

service squid restart

Now we can access ftp port particular ipaddress with particular domain/website of the network.