How to install & configure sarg ?

Step :1 Installed required package

  First we need to install the required package for sarg squid analysis report generator.

 #yum install gcc gd gd-devel make perl-GD wget

Step :2 Install Sarg

   Sarg package can be easily install from the default repositories using yum package manager

#yum install sarg

 The default epel repository provide the sarg package.

Step :3 Configuration of Sarg

  Now we need to edit sarg configuration file. Open the sarg main conf file with your editor.

#vim /etc/sarg/sarg.conf

Uncomment and add the original path of your squid.log file.

“ access_log /var/log/squid/access/log ”

Next, output directory path to save the generate squid report in that directory.

“ output_dir /var/www/sarg/ ”

Set the data formate for sarg report

“ date_format e “

Use userid instead IP address in reports

“ user_ip yes “

set the users exclude file from reports

“exclude_users /etc/sarg/exclude.users “

uncomment and set the overwrite report to yes

“ overwrite_report yes”

That’s it save and close file.

Step :4 Generating the Sarg Report

  Once completed a sarg configuration file, To run the following command to generate the sarg squid analysis report.

#sarg -x

Output

SARG: Init
SARG: Loading configuration from /etc/sarg/sarg.conf
SARG: Loading exclude file from: /etc/sarg/exclude.users
SARG: Parameters:
SARG: Hostname or IP address (-a) =
SARG: Useragent log (-b) =
SARG: Exclude file (-c) =
SARG: Date from-until (-d) =
SARG: Email address to send reports (-e) =
SARG: Config file (-f) = /etc/sarg/sarg.conf
SARG: Date format (-g) = Europe (dd/mm/yyyy)
SARG: IP report (-i) = No
SARG: Input log (-l) = /var/log/squid/access.log
SARG: Resolve IP Address (-n) = Yes
SARG: Output dir (-o) = /var/www/sarg/ONE-SHOT/
SARG: Use Ip Address instead of userid (-p) = No
SARG: Accessed site (-s) =
SARG: Time (-t) =
SARG: User (-u) =
SARG: Temporary dir (-w) = /tmp/sarg
SARG: Debug messages (-x) = Yes
SARG: Process messages (-z) = No
SARG:
SARG: sarg version: 2.3.1 Sep-18-2010
SARG: Reading access log file: /var/log/squid/access.log
SARG: Records in file: 132877, reading: 100.00%
SARG: Records read: 132883, written: 132417, excluded: 466
SARG: Squid log format
SARG: Period: 06 Nov 2017
SARG: pre-sorting files
SARG: File /var/www/sarg/ONE-SHOT/06Nov2017-06Nov2017 already exists, moved to /var/www/sarg/ONE-SHOT/06Nov2017-06Nov2017.3
SARG: Making file: /tmp/sarg/192_168_2_3
SARG: Making file: /tmp/sarg/192_168_2_19
SARG: Making file: /tmp/sarg/192_168_2_160
SARG: Making report: 192.168.2.64
SARG: Making index.html
SARG: Purging temporary file sarg-general
SARG: End
Step :5 Access the Sarg Report

 The generated report placed under the localhost root directory /var/www/sarg/index.html or /var/www/html/sarg/index.html that can accessed by following address

http://www.sarg.local

or

https://www.sarg.local

Step :6 Automatic Generating Sarg Report

  To automatic generating the sarg report to given the time by using cron job.

Example

#crontab -e

add the following line at the end of the file

00 10 * * * /usr/local/bin/sarg -x

save and close it.

The above cronjob will generate the report everyday at 10’o clock.